## Slide 1: Transaction level modelling
TLM2 based system models in practice

## Slide 2: Agenda
  Modelling at RTL level + hands-on (1h)
  The need for higher levels of abstraction: why and how (30’)
  Coffee break (15’)
  TLM2 concepts: interfaces, sockets, coding styles (30’)
  The loosely timed coding style + hands-on (1h)
  Lunch (1h)
  The approximately timed coding style + hands-on (1h15)
  Coffee break (15’)
  Interconnect and architectural exploration + hands-on (1h30)
  ending notes: a real system, further information (30’)

## Slide 3: Agenda
  Modelling at RTL level + hands-on
  The need for higher levels of abstraction: why and how
  Coffee break
  TLM2 concepts: interfaces, sockets, coding styles
  The loosely timed coding style + hands-on
  Lunch
  The approximately timed coding style + hands-on
  Coffee break
  Interconnect and architectural exploration + hands-on
  ending notes: a real system, further information

## Slide 4: Modelling two communicating blocks: HDL abstraction level
Using signals to connect blocks
Notes: A low level system-C implementation with two block doing a simple communication with signals

## Slide 5: Modelling two communicating blocks: HDL abstraction level
Using signals to connect blocks
Example system:
Master
Reset
Slave
Clock
start
done
clock
resetn
Notes: A low level system-C implementation with two block doing a simple communication with signals

## Slide 6: Slave behaviour
Behaviour after reset (repeated) :
  Wait for start signal
  Deassert done and clear sum
  Add 10 terms to the sum, one per cycle
  Assert done

## Slide 7: Master behaviour
Behaviour after reset:
  Count 50 cycles
  Start slave
  Wait until slave is ready
  Repeat 5 times

## Slide 8: Implementation
example1
  Toplevel
    top.h
    top.cpp
  Slave : interface and implementation of the slave block
    slave.h
    slave.cpp
  Master: interface and implementation of the master block
    master.h
    master.cpp

## Slide 9: Hands-on : working with low level models
Modify the example:
  Make start signal a 12-bit wide unsigned integer
  Add the value of the start signal as an extra term to the sum
  Add a 16-bit wide unsigned integer signal to transfer the resulting sum
Notes: Took me about 20’ (+ 5’ Makefile adjustment, nicely printing results)

## Slide 10: Structure of the examples
  main.cpp
    generic simulation set-up: sc_main function instantiating top modules and starting simulation
  top.h top.cpp
    interface and implementation of the example
    public interface is generic
    implementation is specific per example (every example instantiates and connects specific modules)

## Slide 11: Structure of the examples: Makefile
  Makefile targets:
    clean
      remove generated binaries (triggering full rebuild)
    very_clean
      remove more generated stuff (cleaning to original state)
    build (default)
      build example binary
    run
      run example binary

## Slide 12: Hands-on preparation
  Create and go to working directory
    mkdir /scratch/<login>
    cd /scratch/<login>
  Get sources
    tar xfz ~glasseem/tlm_course.tgz
    cd tlm_course
  Set-up environment
    source tlm_course_setup.csh
Notes: Solution in exercise1

## Slide 13: Hands-on: possible implementation
exercise1
  Toplevel
    top.h
    top.cpp
  Slave :
    slave.h
    slave.cpp
  Master:
    master.h
    master.cpp
Notes: Deel 1 : 15’ example 1, 30’ hands-on werk, 15’ bespreking resultaten

## Slide 14: Too detailed for real world blocks and systems
A real system: some memory-mapped registers
Master
Reset
Slave
Clock
done
clock
resetn
read_ena
write_ena
addr
write_data
read_data
ready
Notes: Adding a memory mapped interface, low level,

## Slide 15: Implementation
example2
  Toplevel
    top.h
    top.cpp
  Slave : interface and implementation of the slave block
    slave.h
    slave.cpp
  Master: interface and implementation of the master block
    master.h
    master.cpp

## Slide 16: Problems with this modelling style
  You have to specify a full bus protocol
    Spending a lot of thought on signals
      Which signals
      Signal width
      Exact signal timing
    You may want to interface through an off-the-shelve bus protocol (AHB, AXI, OCP, ...)
    This may not be known yet (e.g. during architecture exploration)
  A lot of inefficient development time
  Signal toggling simulates slow

## Slide 17: Agenda
  Modelling at RTL level + hands-on
  The need for higher levels of abstraction: why and how
  Coffee break
  TLM2 concepts: interfaces, sockets, coding styles
  The loosely timed coding style + hands-on
  Lunch
  The approximately timed coding style + hands-on
  Coffee break
  Interconnect and architectural exploration + hands-on
  ending notes: a real system, further information

## Slide 18: Enter transaction level modelling
  Blocks communicate with transactions over memory- mapped bus:
    Write values to registers
    Read values from registers
    Trigger behaviour that requires an amount of time

## Slide 19: TLM2 example system
Master
Slave
done
initiator
target

## Slide 20: A TLM2 example : implementation
example3
  Toplevel
    top.h
    top.cpp
  Slave : interface and implementation of the slave block
    slave.h
    slave.cpp
  Master: interface and implementation of the master block
    master.h
    master.cpp
Notes: A tlm2 block with a couple of registers.

## Slide 21: Transaction level modelling: use cases
  Architecture exploration
  Software development
  ( Verification)

## Slide 22: Architectural exploration traditionally
  Traditional HDL based design flows: too low level for architectural exploration:
    Architectural level trade-offs are hidden in implementation detail
    Design cycle is too long for exploring architectural options
    Simulation times too long for exploration
  Traditional solution:
    Using back-of-the-envelop calculations, spreadsheets and drawings
    “Gut” feeling, with safety margins.
    Little room/time for architectural optimisation through exploration
  Risks:
    only local optimisations very far in the design process
    a bad architectural choice is exposed very late, causing a long delay
    a highly suboptimal design

## Slide 23: Architectural exploration with TLM
  Higher abstraction level allows for faster development, faster exploration of architectural options
  The architectural choices more visible
  Hard to estimate power accurately at this level
  Good timing estimates are essential

## Slide 24: Software development traditionally
  Testing and debugging of software can only start when HDL simulation/emulation model/ actual hardware is available
  This sequential flow leads to long time-to-market
  Simulation is fairly slow, due to low level implementation details (pin wiggling)
  Low-level debugging much harder
  Emulation requires expensive hardware and tools

## Slide 25: Software design using TLM
  Due to high level of abstraction, the model can be available much earlier in the design phase
  Debugging on higher abstraction layer is easier
  Depending on abstraction layer, it simulates (much) faster
  Need to maintain an additional model

## Slide 26: Software development
HDL design
Back End
Specification
Integration
Software development
HDL design
Back End
Specification
Integration
Software dev
TLM
Traditional HDL based flow
TLM based flow
Notes: Basic statement: Software dev can start much earlier and can go smoother because of faster simulations
Only works if TLM is indeed available much faster, and if the integration effort does not become bigger because of TLM/hardware inconsistencies
It should also allow more extensive testing of the design before sign-off
The additional advantage is that the TLM can serve as a reference/spec for the HDL, which is much more formal
A verification method around it supporting both

## Slide 27: Different approaches to TLM
  Define your own transaction level modelling API
    C, C++, systemC based
    Full control often leading to optimal simulation speed
    No tool vendor dependence
    No tool vendor support
    Reuse of external models require lot of integration work
  Use tool vendor API and models (e.g. Synopsys)
    Good model availability for off-the-shelf components
      Busses, processors, ...
    Manual work to integrate models from other providers
    Tool vendor dependence

## Slide 28: Different approaches to TLM
  TLM2 based modelling
    Standardised interface: easy integration of external models
    Good support in EDA tools (e.g. Synopsys, Cadence)
    Open reference implementation available
    No tool vendor dependence
    Different coding styles for different levels of abstraction supported (loosely timed, approximately timed)
    Combining models of different abstraction levels possible

## Slide 29: TLM2 in Synopsys

## Slide 30: Virtual Platform Characteristics
Instruction Set Simulator | TLM | RTL
Available early | Available early | Much Later
Fast enough to run applications | Fast enough to run applications | Too slow to run applications
No/little hardware details | Register Accurate | Register and Pin accurate
No timing | Timing if needed | Cycle Accurate

## Slide 31: Agenda
  Modelling at RTL level + hands-on
  The need for higher levels of abstraction: why and how
  Coffee break
  TLM2 concepts: interfaces, sockets, coding styles
  The loosely timed coding style + hands-on
  Lunch
  The approximately timed coding style + hands-on
  Coffee break
  Interconnect and architectural exploration + hands-on
  ending notes: a real system, further information

## Slide 32: Agenda
  Modelling at RTL level + hands-on
  The need for higher levels of abstraction: why and how
  Coffee break
  TLM2 concepts: interfaces, sockets, coding styles
  The loosely timed coding style + hands-on
  Lunch
  The approximately timed coding style + hands-on
  Coffee break
  Interconnect and architectural exploration + hands-on
  ending notes: a real system, further information

## Slide 33: SystemC terminology
  Module
    The basic building block of systems modelled in systemC
    All other system components are incorporated within modules (including submodules)
    May contain one or more processes
  Interface
    Abstract data type separating processing from communication
    Implemented by one or more channels
  Channel
    Mechanism for communication between processes (of a single module or within different modules)
    Implements one or more interfaces
Notes: Interfaces are normative, coding styles not, sockets are bound to interface

## Slide 34: SystemC terminology (ctd)
  Port
    Mediator for communication between modules
    Indicates that the modules requires an interface
    Forwards interface method calls up or out of the module
    Class templated with the interface type
  Export
    Mediator for communication between modules
    Indicates that the modules provides an interface
    Forwards interface method calls down or into the module
    Class templated with the interface
Notes: Interfaces are normative, coding styles not, sockets are bound to interface

## Slide 35: Terminology: example
Master
Reset
Slave
Clock
start
done
clock
resetn
Top
Modules
Notes: Reusing the example to clarify systemC terminology: modules

## Slide 36: Example revisited
example1
  Toplevel
    top.h
    top.cpp
  Slave : interface and implementation of the slave block
    slave.h
    slave.cpp
  Master: interface and implementation of the master block
    master.h
    master.cpp
Notes: Reusing the example to clarify systemC terminology: ports, interfaces, exports, signals.

## Slide 37: TLM2 interfaces: the blocking transport interface template
  Template interface defining
    virtual void b_transport(TRANS & trans, sc_core::sc_time & t) = 0
      References for simulation speed
      Called in initiator, from a thread process
      Implemented in target
      Time parameter allows for “temporal decoupling”
      Two timepoints per transaction
        Time of call
        Time of return

## Slide 38: TLM2 Interfaces: the non-blocking transport interface templates
  Forward interface template defining
    virtual tlm_sync_enum nb_transport_fw (TRANS & trans, PHASE &ph, sc_core::sc_time & t) = 0
    Called by initiator, in a method or thread process
    Implemented in target module
  Backward interface template defining
    virtual tlm_sync_enum nb_transport_bw (TRANS & trans, PHASE &ph, sc_core::sc_time & t) = 0
    Called by target in a method or thread process
    Implemented in initiator module

## Slide 39: TLM2 Interfaces: template arguments
  Template parameter TRANS should be tlm_generic_payload for maximum compatibility
  Template parameter PHASE should be tlm_phase for maximum interoperability
    Defining the 4 timepoints of a transaction using the base protocol : BEGIN_REQ, END_REQ, BEGIN_RESP, END_RESP
  For modelling exotic protocols, other template parameters are allowed, at expense of compatibility

## Slide 40: Other TLM2 interfaces
  Debug interface template defining
    virtual unsigned int transport_dbg(TRANS &trans)=0
    For debug accesses (without timing, without side effects )
  Direct memory interface templates
    Allowing an initiator to bypass interconnect and directly access the memory of a target
    A forward interface defining
      virtual bool get_direct_mem_ptr(TRANS &trans, tlm_dmi & dmi)=0
    A backward interface defining
      virtual void invalidate_direct_mem_pointer(sc_dt::uint64 start_range, sc_dt::uint64 end_range)=0

## Slide 41: Combined TLM2 interfaces
  TLM2 forward interface combines
    Blocking transport interface
    Non-blocking forward transport interface
    Forward direct memory interface
    Debug interface
  TLM2 backward interface combines
    Non-blocking backward transport interface
    Backward direct memory interface

## Slide 42: Sockets
  Combine a port and an export
  Target socket (tlm_target_socket)
    An export providing the TLM2 forward interface
    A port requiring the TLM2 backward interface
  Initiator socket (tlm_initiator_socket)
    A port requiring the TLM2 forward interface
    An export providing the TLM2 backward interface
  Binding an initiator socket to a target socket binds two port-export pairs
  Required for TLM2 interoperability (in tlm namespace)
  Buswidth as template parameter
Notes: Combine port and exports, target socket, initiator socket, convenience socket

## Slide 43: Convenience sockets a.k.a simple sockets
  simple_initiator_socket<> and simple_target_socket<>
  Derived from tlm_initiator_socket and tlm_target_socket respectively
  Utilities for easier implementation (in tlm_utils namespace)
  Not required for TLM2 compatibility
  Provide automatic conversion between non-blocking and blocking transport calls (i.e. Requiring only one of both)

## Slide 44: A target device
  With plain socket
    Module with target socket
    Inherit from and implement forward transport interface tlm_fw_transport_interface (or create subclass for this)
    Bind socket to this pointer (or to an object of the subclass)
  With convenience socket
    Module with target socket
    Create member functions for transport callbacks
    Register callback functions
Notes: Plain socket: every callback has to be implemented, convenience socket convert blocking<->non-blocking if only one is provided

## Slide 45: An initiator device
  With plain socket
    Module with initiator socket
    Inherit from and implement backward transport interface tlm_bw_transport_interface (or create subclass for this)
    Bind socket to this pointer (or to an object of the subclass)
    Initiator thread uses forward interface calls to communicate with target modules
  With convenience socket
    Module with initiator socket
    Create member functions for callbacks
    Register callback functions
    Initiator thread uses forward interface calls to communicate with target modules
Notes: With convenience sockets, only the callbacks that will occur are needed

## Slide 46: Generic Payload
  Main content of transactions
  Contains usual information for memory mapped bus systems:
    Address
    Data (for read and write)
    Command (read, write, ignore)
    Length
    Streaming width
    Byte enable
    response
  Extension mechanism available

## Slide 47: Coding styles
  Suggested approaches for modelling systems
  Not required for TLM2 compliant models.
  Two styles
    Loosely timed coding style
    Approximately timed coding style

## Slide 48: Agenda
  Modelling at RTL level + hands-on
  The need for higher levels of abstraction: why and how
  Coffee break
  TLM2 concepts: interfaces, sockets, coding styles
  The loosely timed coding style + hands-on
  Lunch
  The approximately timed coding style + hands-on
  Coffee break
  Interconnect and architectural exploration + hands-on
  ending notes: a real system, further information

## Slide 49: Loosely timed coding style
  Appropriate for use cases only requiring coarse grain timing accuracy
  Simple to implement
  Only using blocking transports, but preferably without blocking
  Using temporal decoupling
  Limiting context switching
  Fast simulations

## Slide 50: Loosely timed coding style
Initiator
Target
b_transport(trans, 0 ns)
return(trans, 10 ns)
Simulation time
10 us
11 us
wait(1000 ns)
b_transport(trans, 40 ns)
return(trans, 60 ns)
b_transport(trans, 990 ns)
return(trans, 1000 ns)
b_transport(trans, 0 ns)
return(trans, 10 ns)
...
...

## Slide 51: Loosely timed coding style example
example3
  Toplevel
    top.h
    top.cpp
  Slave : interface and implementation of the slave block
    slave.h
    slave.cpp
  Master: interface and implementation of the master block
    master.h
    master.cpp

## Slide 52: Hands-on: a system in loosely timed coding style
Starting with example3:
  Split the TLM2 interface between a control and data interface
    Data interface containing the values to be added
    Control interface containing a register to start the slave, and a register to read back the result
Notes: Took me 40’

## Slide 53: Hands-on: possible implementation
exercise2
  Toplevel
    top.h
    top.cpp
  Slave :
    slave.h
    slave.cpp
  Master:
    master.h
    master.cpp

## Slide 54: Agenda
  Modelling at RTL level + hands-on
  The need for higher levels of abstraction: why and how
  Coffee break
  TLM2 concepts: interfaces, sockets, coding styles
  The loosely timed coding style + hands-on
  Lunch
  The approximately timed coding style + hands-on
  Coffee break
  Interconnect and architectural exploration + hands-on
  ending notes: a real system, further information

## Slide 55: Agenda
  Modelling at RTL level + hands-on
  The need for higher levels of abstraction: why and how
  Coffee break
  TLM2 concepts: interfaces, sockets, coding styles
  The loosely timed coding style + hands-on
  Lunch
  The approximately timed coding style + hands-on
  Coffee break
  Interconnect and architectural exploration + hands-on
  ending notes: a real system, further information

## Slide 56: Approximately timed coding style
  Appropriate for use cases requiring fine grain timing accuracy
  Harder to implement
  Using non-blocking transports
  More context switching
  Simulating slower
  Requires memory management for transactions

## Slide 57: Approximately timed coding style
Initiator
Target
nb_transport_fw(trans, BEGIN_REQ,0 ns)
accepted
accepted
nb_transport_bw(trans, END_REQ,0 ns)
Simulation time
10 us
10,100 us
wait(10 ns)
10,010 us
wait(50 ns)
accepted
nb_transport_bw(trans, BEGIN_RSP,0 ns)
10,060 us
wait(40 ns)
nb_transport_fw(trans, END_RESP,0 ns)
accepted

## Slide 58: Approximately timed coding style: early termination
Initiator
Target
nb_transport_fw(trans, BEGIN_REQ)
completed
updated(trans, END_RESP)
nb_transport_bw(trans, BEGIN_RESP)
nb_transport_fw(trans, BEGIN_REQ)
updated(trans, END_REQ)

## Slide 59: Approximately timed coding style: pipelined transactions
Initiator
Target
updated(trans1, END_RESP)
nb_transport_bw(trans1, BEGIN_RESP)
nb_transport_fw(trans1, BEGIN_REQ)
updated(trans1, END_REQ)
completed(trans2)
nb_transport_bw(trans2, BEGIN_RESP)
nb_transport_fw(trans2, BEGIN_REQ)
updated(trans2, END_REQ)

## Slide 60: Combining approximately timed and loosely timed models
  Simple sockets take care of conversion
  Accuracy limited by least accurate model (loosely timed)
  Simulating time close to slowest model (approximately timed)
  Reuse of models possible
  Loosely timed initiator - approximately timed target: example4
  Approximately timed initiator – loosely timed target: example5

## Slide 61: Modelling an Approximately timed system
example6
  Toplevel
    top.h
    top.cpp
  Slave : interface and implementation of the slave block
    slave.h
    slave.cpp
  Master: interface and implementation of the master block
    master.h
    master.cpp
Notes: Same system as the original system, but in AT

## Slide 62: Hands-on approximately timed coding style
Start from example 7:
  Per iteration, all 10 registers of the sum are written consecutively
  Change it so that they are written in a pipelined fashion.
  Hints
    In master, start next transaction after the end of the request, do not wait for end of response.
    Wait for end of response before starting slave
Notes: Write the slave registers in a pipelined fashion

## Slide 63: Hands-on: possible implementation
exercise3
  Toplevel
    top.h
    top.cpp
  Slave :
    slave.h
    slave.cpp
  Master:
    master.h
    master.cpp

## Slide 64: Agenda
  Modelling at RTL level + hands-on
  The need for higher levels of abstraction: why and how
  Coffee break
  TLM2 concepts: interfaces, sockets, coding styles
  The loosely timed coding style + hands-on
  Lunch
  The approximately timed coding style + hands-on
  Coffee break
  Interconnect and architectural exploration + hands-on
  ending notes: a real system, further information

## Slide 65: Agenda
  Modelling at RTL level + hands-on
  The need for higher levels of abstraction: why and how
  Coffee break
  TLM2 concepts: interfaces, sockets, coding styles
  The loosely timed coding style + hands-on
  Lunch
  The approximately timed coding style + hands-on
  Coffee break
  Interconnect and architectural exploration + hands-on
  ending notes: a real system, further information

## Slide 66: Modelling interconnect
  A bus model: basically containing one or more initiators and one or more targets, passing transactions from target to initiator.
  A TLM2 interconnect model easily be parametrised to match a specific memory-mapped bus protocol (AHB, AXI, OCP, ...) by setting the correct timing parameters and limiting the amount of pending transactions.
Notes: Modelling a bus

## Slide 67: An example bus model
From example8
  Bus model
    bus.h
  Connectivity defined in top
    top.cpp
    top.h

## Slide 68: Architecture exploration
Master
Slave1
initiator
SlaveN
...
target
initiator
initiator
target
target
Notes: What is the impact of maximum burst length, buswidth, on the overal system performance ?

## Slide 69: Architecture exploration
Master
Slave1
initiator
SlaveN
...
target
initiator
initiator
target
target
Number of slaves ?
Buswidth ?
Bus speed ?
Slave speed ?
...
Notes: What is the impact of maximum burst length, buswidth, on the overal system performance ?

## Slide 70: Architecture exploration hands-on
From example9:
  Investigate impact of number of slaves, bus width and bus timing parameters on total time

## Slide 71: Agenda
  Modelling at RTL level + hands-on
  The need for higher levels of abstraction: why and how
  Coffee break
  TLM2 concepts: interfaces, sockets, coding styles
  The loosely timed coding style + hands-on
  Lunch
  The approximately timed coding style + hands-on
  Coffee break
  Interconnect and architectural exploration + hands-on
  ending notes: a real system, further information

## Slide 72: A real system: a wireless baseband system

## Slide 73: Quantum keeper
  Convenience utility to manage the amount of temporal decoupling (in tlm_utils namespace)
  Class tlm_quantum_keeper
    Static void set_global_quantum(const sc_time&)
      Set time processes can run ahead
    void inc(const sc_time&),void set(const sc_time&)
      Increment local time, set local time
    sc_time get_local_time(), sc_time get_current_time()
      Get local time offset, Get total time
    bool need_sync()
      Local time offset exceeds quantum, sync needed
    void sync()
      Yield, i.e. wait until systemC time catches up

## Slide 74: Payload event queue
  Convenience utility for managing events associated with a transaction (in tlm_utils namespace)
  Templated with transaction type (typically tlm_generic_payload)
  Two types :
    Class peq_with_get
    Class peq_with_cb

## Slide 75: Payload event queue
  peq_with_get:
    notify(TRANS &, const sc_time&) puts the event and the transaction on the queue to occur after the specified time
    sc_event& get_event() returns event that will trigger
    TRANS* get_next_transaction() returns transaction, or 0 if none
  Class peq_with_cb_and_phase
    Callback cb registered in constructor
    notify(TRANS&, PHASE&, const sc_time&) puts event with associated transaction and phase in queue
    cb(TRANS&, PHASE&) gets called when event occurs

## Slide 76: Additional resources
The accellera website (www.accellera.org):
  Former systemc.org
  Open source systemC and TLM2 reference implementations
    Including examples on approximately and loosely timed coding
  Video tutorials
  The systemC and TLM2 language reference manual (IEEE standard 1666-2011)